## Slide 1
Smart-RUDP
Reliable UDP with learning-based congestion control, in C
Computer Networks | Faculty: Anuradha G
Harshavardhan Mallela 24BAI0274 Rohit Arya 24BCE0819 Shloak Sinha 24BDS0378

## Slide 2
The problem
2 / 21 Smart-RUDP
UDP
Fast and simple, but no guarantees: packets can be lost, duplicated or reordered.
TCP
Reliable, but lives inside the OS kernel. Hard to see, hard to change, hard to learn from.
In 1986 the early Internet suffered congestion collapse: throughput fell from 32 Kbps to 40 bps. TCP congestion control was invented to fix it.
Our question: can we rebuild TCP's core ideas ourselves, on top of UDP?

## Slide 3
Why we built it
3 / 21 Smart-RUDP
The need
Campus users send data to a server across a routed network. TCP is fixed inside the kernel; plain UDP gives no guarantees. Real systems (QUIC, HTTP/3) solve this with reliability built in user space over UDP.
Our answer
RUDP: a readable, tunable reliable transport over UDP, plus Smart-RUDP, a controller that learns the window from RTT and loss.
Scenario: a student on VLAN 10 uploads a file to the server LAN. The ACL keeps students out of staff VLAN 20. If a core link fails, OSPF reroutes through R2: a longer path and higher RTT that the transport must adapt to.
Validated: protocol tests and Smart-RUDP vs AIMD on emulated paths; network design built and tested in Packet Tracer; traffic analysed in Wireshark.

## Slide 4
What we built
4 / 21 Smart-RUDP
Handshake
SYN, SYN-ACK, ACK before any data flows.
Reliability
Sequence numbers, ACKs, checksums, timeouts, retransmission.
Flow control
Go-Back-N sliding window; its size is the congestion window.
Congestion control
AIMD: slow start, avoidance, halve on loss.
About 670 lines of C across 4 source files. Client + server, built in 8 phases, on github.com/Capsturrrr/rudp

## Slide 5
The RUDP packet header: 13 bytes
5 / 21 Smart-RUDP
Field | Size | Purpose
seq | 4 B | Packet number
ack | 4 B | Next packet expected
flags | 1 B | SYN / ACK / FIN / DATA
checksum | 2 B | Detects corruption
payload_len | 2 B | Data length (max 512)
Fields packed byte by byte, so compiler struct padding never changes the wire format.
Data packet = 53 bytes on the wire. ACK / handshake = 13 bytes.

## Slide 6
Handshake and data flow
6 / 21 Smart-RUDP
1
SYN
Client -> Server
Request a connection
2
SYN-ACK
Client <- Server
Server agrees
3
ACK
Client -> Server
ESTABLISHED, data may flow
4
DATA
Client -> Server
Up to window-size packets in flight
5
ACK
Client <- Server
Cumulative: confirms everything up to N
6
FIN
Client -> Server
Close the connection
Server accepts a new SYN in any state, so a killed client can never leave it stuck.

## Slide 7
Reliability: Go-Back-N
7 / 21 Smart-RUDP
Window = cwnd packets in flight (fixed at 4 in Phase 4, then driven by cwnd)
Receiver sends cumulative ACKs
Retransmission timeout: 500 ms
Fast retransmit after 3 duplicate ACKs, no waiting for the timer
Checksum failures are dropped, then recovered by retransmission
Proof
In a netem 20% loss capture we saw 12 timeouts spaced about 500 ms apart.
Result
2,442-byte message reassembled correctly.

## Slide 8
Congestion control: AIMD
8 / 21 Smart-RUDP
Fresh runs at 0%, 10%, 20% and 40% simulated loss. Red = timeout, green = fast retransmit.
Slow start: cwnd +1 per ACK, below ssthresh 16
Avoidance: cwnd + 1/cwnd per ACK
3 dup ACKs: cwnd halves
Timeout: cwnd resets to 1, ssthresh halves
Capped at 32

## Slide 9
How we tested
9 / 21 Smart-RUDP
Built-in loss simulator
Drops packets in code at a set percentage. Used for the benchmark.
tc / netem
Linux kernel injects real loss on loopback. Used to validate behaviour.
Wireshark / tshark
Captured in WSL, opened in Windows Wireshark. Confirmed handshake, ACKs, retransmissions.
Wireshark could not see WSL loopback from Windows, so we captured with tshark inside WSL and copied the file across.

## Slide 10
Benchmark results
10 / 21 Smart-RUDP
62 of 62 packets delivered at every loss level, from 0% to 40%.

## Slide 11
Problems we hit and fixed
11 / 21 Smart-RUDP
Problem | Fix
Server stuck after killed client | Accept SYN in any state (was a 15.5 s hang)
Leftover netem rule | Check tc qdisc show dev lo, delete before each test
Windows Wireshark saw nothing | Capture with tshark inside WSL, then copy
Shell portability in benchmark | Replaced date/grep tricks with awk and sed

## Slide 12
Literature behind the design
12 / 21 Smart-RUDP
Jacobson & Karels (1988): congestion avoidance and control, the origin of AIMD
Chiu & Jain (1989): why additive increase, multiplicative decrease converges fairly
RFC 5681 (2009): TCP congestion control standard
Ha, Rhee, Xu (2008): CUBIC, our future-work direction
Langley et al. (2017) and RFC 9000: QUIC, reliable transport over UDP in production
Midhula & Arun Raj Kumar (2024) and Cao et al. (2023, DRLFcc): deep reinforcement learning for congestion control, the idea behind Smart-RUDP
Key researcher: Van Jacobson

## Slide 13
Network design: OSPF topology in Packet Tracer
13 / 21 Smart-RUDP
4 routers, OSPF area 0 (R1-R2-R3 triangle, R4 branch)
2 VLANs, router-on-a-stick, DHCP on R1 and R4
Access list: student to staff blocked (verified)
Routes: server LAN metric 2 via R3, branch metric 3 via R2
Failover: shut R1 Gi0/2, 70/71 pings, reroute via R2 (metric 3)
Built and tested in Packet Tracer: OSPF adjacencies, routes, ACL and failover all verified.

## Slide 14
Packet Tracer results: routes, failover, ACL
14 / 21 Smart-RUDP
OSPF routes on R1
Link failure: 70/71 pings, reroute
ACL: student blocked, staff allowed
Server LAN metric 2 via R3, branch LAN metric 3 via R2
Shutting R1 Gi0/2: traffic reroutes via R2, only 1 of 71 pings lost
Student PC gets "destination unreachable" to staff; server still reachable (TTL 126)

## Slide 15
Smart-RUDP: a Q-learning window controller
15 / 21 Smart-RUDP
State (80)
RTT ratio x loss fraction x window size, sampled once per RTT.
Action (5)
Multiply cwnd by 0.5, 0.85, 1.0, 1.15 or 1.5.
Reward
Throughput gained, minus delay growth, minus retransmissions.
Same Go-Back-N reliability as the baseline; only the window policy changes. Paths emulated in-program: 5G-like, lossy wireless, satellite-like.

## Slide 16
Smart-RUDP vs AIMD: honest result
16 / 21 Smart-RUDP
6 evaluation runs per scenario after 40 training episodes
Not faster: +63% time on 5G-like, +10% on satellite, tie on lossy
Fewer retransmissions on 5G-like and satellite, but within run-to-run noise
Earlier training rounds were much worse; reported run is the final configuration

## Slide 17
Wireshark: RUDP dissector and traces
17 / 21 Smart-RUDP
rudp.lua decodes seq, ack, flags, checksum, length
Filters: smartrudp.flags.data == 1, smartrudp.seq == N
400 packets, lossy path: 87 (AIMD) and 95 (Smart) repeated data segments seen at the receiver
Trace exported by the program, topology addresses, handshake not included

## Slide 18
Wireshark: real capture
18 / 21 Smart-RUDP
Left: SYN, SYN-ACK, ACK decoded by the smartrudp dissector (filter frame.number <= 3)
Right: smartrudp.seq == N shows the same segment sent twice, a retransmission

## Slide 19
Demo: RUDP Chat over the internet
19 / 21 Smart-RUDP
Each message is one RUDP segment: numbered, checksummed, ACKed in order
Browser UI via a small gateway; terminal version too
Two machines linked over Tailscale (laptop and phone)
Loss slider: lost messages are resent and still arrive in order
Uses a fixed window of 8, not the Smart-RUDP controller

## Slide 20
Learnings and future work
20 / 21 Smart-RUDP
Learned
Reliability is a set of simple rules working together.
Congestion control matters as much as retransmission.
Testing tools fail in surprising ways.
Next
Selective Repeat / SACK
A stronger learning agent
Kernel netem and real multi-machine tests
Run RUDP across a real multi-machine network
Limits: Go-Back-N wastes bandwidth; emulated (not kernel) paths; Smart-RUDP did not beat AIMD.

## Slide 21
Thank you
github.com/Capsturrrr/rudp
Harshavardhan Mallela Rohit Arya Shloak Sinha

## Slide 22
Appendix: slow start and congestion avoidance
Appendix Smart-RUDP
cwnd starts at 1
+1 per ACK until ssthresh = 16
Then +1/cwnd per ACK
62 packets, final cwnd 18.71